Advanced Energy Panel Specifications (Currently designed for energy savings in cold climates)

See: http://www.windotherm.com/Replacement-windows-howitworks.htm

Question:

Is there a durable, shrinkable film that can be applied on the outside portion of the extrusion (that which would be facing towards the outside of the house) that can serve as a solar block for hot climates?

The window insulation panel is for application to the interior side of an existing window.

Current Materials

  - Glazing shall be TWO layers of 1mil, triple layer, extruded, cross-linked Polyolefin with haze of 2.7% or less, instrumented impact of 28.5 pounds or more, tensile strength of 15,200 psi or greater and a shrink factor of 13 to 22% at 200 degrees F.

  - Frame rails, stiles, and muntins shall be extruded aluminum, 7/16" x ¾" in exterior dimension, .060" wall thickness, provided with glazing retention grooves on two opposite sides.

  - Frame shall be weatherstripped on all surfaces which contact primary window frame.

  - Metal frame shall be finished with durable white or brown paint.

  - Corner fasteners shall be structural nylon in matching colors.

  - Mullions shall be formed H-channels capable of sealing and securing adjacent panel sections and shall be color matched.

Construction

  - Panel shall be added as a supplement on the interior side of an existing exterior window.

  - Panel shall be custom built to match exact fit with existing window.

  - Mounting options shall include a choice of front surface mount or recessed inside the jambs.

  - Panels shall be easy to remove and replace, needing only a screwdriver or no tools, depending on configuration.

  - Panels may optionally have provision for self-storing of sub-panels in place upon each other, and for creating modular coverage of very large (ten feet by ten feet or larger) window areas.

  - Panel shall be built with two essentially clear and airtight glazing surfaces, plus a perimeter draft stop of compressible weatherstrip material.

Performance

  - Panel shall provide immediate comfort and energy savings.

  - Panel shall virtually stop drafts and air infiltration.

  - Tested insulation value shall outperform Energy Star northern zone criteria panel in combination with existing windows shall have a tested U-factor of .31 or less.

  - Panel shall have a minimal visual effect upon the exterior architecture, and minimal and totally reversible effect on interior architecture.

  - Panel shall reduce condensation and noise.

  - Glazing material shall have high clarity.

  - Glazing material shall have the ability to withstand the impact of a 50mph regulation baseball without breaking.

Fire and smoke hazards shall be minimal: glazing material shall have a self ignition temperature, per ASTM-D-1929 of no less than 660F; an average time of burn of 5 seconds or less and average extent of burn of 1.4" or less, per ASTM-D-635; and a smoke density, per ASTM-D-2843 of less than 37%.

Please contact: Jon Gorham jon@greenmediaventures.com

203.376.2871	Woodbridge, CT