Deep Energy Retrofits: Six Real World Examples and Lessons Learned

Mike Keesee, Sacramento Municipal Utility District (SMUD)

ABSTRACT

The Obama Administration’s Economic Stimulus Plan contains billions of dollars for improving the energy efficiency of existing homes, while the California Energy Efficiency Strategic Plan calls for reducing energy use in existing homes 40% by 2020.How will we get these energy savings out of existing homes?

The Sacramento Municipal Utility District (SMUD) and the National Renewable Energy Laboratory (NREL) have partnered on a research and development program that works with local builders in dramatically improving the energy performance of existing homes. These “Deep Energy Retrofits” feature advanced construction techniques and energy efficiency measures designed to reduce an existing home’s energy use by 50% or more. This paper describes six completed DER demonstration projects, monitoring results to date, and lessons learned. Results from these DER demonstration projects suggest that utility whole house performance programs should focus on developing climate zone specific energy efficiency packages and target un-served utility customer markets, including the existing home re-sale market, especially foreclosures, and re-modeling projects.  In particular combining an energy efficient mortgage at re-sale with state and utility home performance programs represent a huge untapped opportunity to gain cost effective energy savings.

Background

SMUD’s Energy R&D program partnered with the National Renewable Energy Laboratory (NREL) to develop a new approach to achieving dramatic energy savings in existing homes,  “Deep Energy Retrofits” (DERs) and demonstrate the results.  SMUD and NREL set a simple design goal for the demonstration program: reduce an existing home’s total energy use by at least 50 percent. To achieve this goal meant using a whole house (or systems) methodology to retrofit the home.  DERs can also involve major remodeling of the home which means dealing with existing conditions that might range from room configuration to hazards such as mold, lead and asbestos.  Six DER projects were completed under the demonstration program. NREL provided energy analysis using its BEopt energy simulation software, including assistance in identifying energy efficiency measures (EEMs), and monitoring services for select DER projects. All the projects incorporated a comprehensive package of EEMs which are described below.  Two projects featured solar PV and/or solar thermal systems.  A summary of results to date will follow DER project descriptions.  The paper will conclude with several “Lessons Learned” from the DER projects.

Market Rate DERs

Two market rate DERs were completed under the DER demonstration program. SMUD collaborated with Greenbuilt, a local home performance contractor, on the first SMUD DER project, a 1980s-era, abandoned, foreclosed all electric, single-story residence undergoing a complete remodel in advance of re-sale. A list of before and after features is found in Table 1 below.

Table 1. Greenbuilt Existing vs. DER Specifications

| System | Existing Features | DER Features |
| --- | --- | --- |
| Ceilings | R-19 | R-42 blown-in cellulose |
| Roofing | Asphalt Composition | Asphalt Composition w/ Radiant Barrier |
| Knee Walls | R-11 | 1" metallic-reflective face Rigid Foam (R-6) over R-15 |
| West Wall | R-11 | R-15 blown in cellulose insulation |
| Infiltration | 6830 CFM @ 50 pa; 21.6 ACH @ 50 pa | 1080 cfm @ 50 pa; 4.1 ACH @ 50 pa |
| Windows & Sliding Glass Door | Aluminum Frame, Single Pane, 1.07 U-Factor: 0.70 SHGC | Vinyl Frame, Dual Pane, Low e, Argon Filled 0.29 to 0.28 U-Factor: 0.22 to 0.19 SHGC |
| Space Heating | HSPF 7.75 | HSPF 9.75 |
| Central A/C | SEER 13/EER 10 | SEER 16/EER 13 |
| Ducts | R-2 insulated in attic | R-6 insulated , "Tight" tested to 4.5% leakage @ 25 Pa in attic |
| Thermostat | Manual | Programmable Communicating Thermostat |
| Whole House Fan | None | Two Speed Whole House Fan |
| Water Htg | .97 Energy Factor Electric Storage Tank | .97 Energy Factor Electric Storage Tank w/ 2.11 Coefficient of Performance (COP) add on Heat Pump |
| Spot Ventilation | None | Energy Start Bathroom Fans with Timer |
| Lighting & Ceiling Fans | Incandescent | 100% hardwired Energy Star Compact Fluorescent & LED Fixtures in master bath |
| SolarTubes | None | Energy Star rated |
| Refrigerator | Existing | Tier 2 (.25% Federal Standards) Energy Star |
| Dishwasher | Existing | Tier 2 (EF = .69) Energy Star |
| Shading on West | None | Retractable Shading w/ wind sensors and timer |
| HERS Score | 182 | 78 |
| Controls | None | Control4 Home Area Network with Wireless “Green” Switch and programmable communicating thermostat |
| Solar Domestic Hot Water | None | 40 gallon Integrated Solar Water Collector 50% Solar Fraction |
| Photovoltaics | None | 2,295 Watt AC Photovoltaic system |

BEopt simulation results showed a 61% reduction in annual energy use and 80% reduction in the home’s peak demand.  The Greenbuilt DER was used as an energy efficiency retrofit showcase by SMUD and  a “lab home” by NREL for one year, September 2009-2010.

32nd Avenue DER

SMUD worked with the Housing Group Fund (HGF) on the second market rate DER, 32nd Avenue. The 32nd Avenue home was an abandoned 1950s vintage, Eichler style 1,340 square foot, single story four-bedroom, two-bath, and 1-car garage tract home requiring extensive renovation.  A list of efficiency measures incorporated into the project is found in Table 2 below.

Table 2.  32nd Avenue Existing Vs. DER Specifications

BY SYSTEM	EXISTING 		ENERGY EFFICIENT REMODEL

Air Sealing	None			Air Sealed the home (caulking and weather-stripping)

Roof  Insulation	None 	 		6” exterior rigid foam (R-38)

Wall Insulation   None,  			4” Quad Lock® exterior rigid foam (EXP) (R-18)

Infiltration          Unknown			1100 cfm @ 50 pa; 6.3 ACH @ 50 pa

Windows 	Aluminum Frame 	Energy Star, Vinyl Frame							single pane, clear		dual pane, low e								1.07 U-value 		0.29 U-value 								0.70 SHGC 		0.24 SHGC

Space Heating	.58 AFUE Gas		0 .95 AFUE Sealed Combustion Gas Furnace				Wall Mounted Furnace

A/C	 	None			SEER 14.5, EER 12

Ducts		None   			 R-6 insulated tested to 3.75%  leakage @ 25 pa in

conditioned  space

Spot Ventilation	None			Energy Start Bathroom Fans with Timer

Water Heating	0.52 EF 50 gal. Gas 	0.62 EF 40 gal. Gas

Lighting 	 Incandescent		100% hardwired Energy Star CFLs

Dishwasher	None			Tier 2 (EF = .69) Energy Star

HERSII Rating	259			80, a 69% improvement

The 32nd Avenue BEopt simulation showed upwards of 66% energy savings, including an estimated electric use savings of 68%, estimated natural gas use savings of 63%, and 82% average peak demand savings . The home renovation was completed in March, 2010 and sold to a first-time home buyer in April, 2010.

Neighborhood Stabilization Program DERs

SMUD partnered with the Sacramento Housing and Redevelopment Agency (SHRA) to improve the energy efficiency of abandoned, foreclosed homes in neighborhoods particularly affected by the recession.  Under SHRA’s Vacant Properties Program (VPP), qualified single-family developers/builders renovate abandoned homes in low income neighborhoods and sell them to qualified low- and middle-income families.  SMUD worked with three VPP contractors, Housing Group Fund (HGF), Del Paso Solutions and the Sacramento Chapter of Habitat for Humanity (HfH).

Mascot DER

Under the VPP, HGF bought an abandoned 1950s vintage single-story 1,260 square foot, four-bedrooms, two-bath home with a two-car garage.  A “package” of energy efficiency measures was installed in the home (see Table 3 below).

Table 3. Mascot Existing Vs. DER Specifications

| SYSTEM | EXISTING FEATURES | DER FEATURES |
| --- | --- | --- |
| Flat Ceilings | R-19 | R-44 blown-in cellulose w/ Radiant Barrier |
| West Wall | R-11 | R-15 blown in cellulose insulation |
| Infiltration | Unknown | 1121 cfm @ 50 pa; 6.7 ACH @ 50 pa |
| Windows | Aluminum Frame Single Pane 1.07 U-Factor; 0.70 SHGC | Energy Star, Vinyl Frame Dual Pane, Low e 0.29 to 0.28 U-Factor; 0.22 to 0.24 SHGC |
| Space Heating | Package Gas .78 AFUE Furnace | Package Gas 0.80 AFUE France |
| A/C | SEER 10/EER 8 | SEER 16/EER 13 |
| Ducts | “Leaky” R-2 ducts in attic | "Tight,” R-6 insulated tested to 3.75% leakage @ 25 Pa |
| Thermostat | Manual | Energy Star Programmable Thermostat |
| Spot Ventilation | None | Energy Star Bathroom Fans with Timer |
| Water Heating | 0.52 Energy Factor 50 gal. Gas Storage Tank | 0.98 Energy Factor Condensing, Tankless Gas Water Heater |
| Lighting & Ceiling Fans | Incandescent | 100% hardwired Energy Star CFLS |
| Dishwasher | None | Tier 2 (EF = .69) Energy Star |
| HERS Score | 241 | 86 |

The BEopt simulation showed annual electricity and natural gas use reduced 47% and 59%, respectively, and 68% average peak demand savings.  HGF completed retrofitting the home in October, 2009 and then sold it to a first-time home-buying family in November 2009. NREL monitored the performance of the condensing tankless gas water heater and published a final report in October, 2011.

Jean Avenue DER

SMUD worked on a second VPP home with Del Paso Solutions.  Under the VPP, Del Paso solutions purchased an all electric, 1040 square foot, 3 bedrooms, and 2 bath, abandoned home on Jean Avenue in the Del Paso Heights neighborhood of Sacramento.  Table 4 shows the energy efficiency upgrades compared to the home’s existing features.

Table 4.  Jean Existing Vs. DER Specifications

BY SYSTEM		EXISTING 			DER FEATURES

Air Sealing		None				Air Sealed the home

Attic Insulation		R-19 	 			15” blown in cellulose (R-49) attic insulation

Room Addition		 NA				2x6, 16” o.c. framing with R-20 cellulose

Infiltration		1880 cfm@ 50 pa			408 cfm @ 50 pa; 						13.6 ACH @ 50 pa		2.9 ACH @ 50 pa

Windows 		Aluminum Frame 		Energy Star, Vinyl Frame						Dual pane, clear 			dual pane, low e							0.71 U-value  			0.32 U-value 							0.73 SHGC 			0.25 SHGC

Space Heating		Heat Pump 			Tri-Zone Mini-split Heat Pump 					7.0 HSPF			9.0 HSPF

A/C	 		3 ton Heat Pump			2 ton Ductless, mini-split Heat Pump				SEER 8, EER 7			SEER 15, EER 9.2

Ducts			Leaky R-2.1 			Ductless

Water Heating		40 gal. Electric 			40 gal. Electric Storage Tank 0.98 Energy Factor			0.90 EF 				with 2.5 COP add on heat pump water heater

Lighting 	 	Incandescent			100% hardwired Energy Star CFLs

Ceiling Fans		Incandescent			Energy Star with pin-based CFLs

HERS Rating		195				86

The Jean Avenue BEopt simulation showed 60% annual energy savings and 67% average peak demand savings. The home was sold and occupied in June, 2011.

Habitat for Humanity (HfH) DER

SMUD worked with the Sacramento Habitat for Humanity (HfH) chapter on abandoned 1946 built 3 bedroom, 1 bath, 1,107 square feet home that required extensive work.  A list of efficiency measures incorporated into the project is found in Table 5 below.

Table 5.  HfH Existing Vs. DER Specifications

BY SYSTEM		EXISTING 		ENERGY EFFICIENT REMODEL

Air Sealing		None			Air Sealed the Home

Floor			Vented 			Conditioned Crawlspace with R-10 Close Cell				Un-insulated 		Spray Foam in the Rim Joists Crawlspace

Roof  Insulation		None  			R-38 with Radiant Barrier

Wall Insulation	Original insulation	R-13 Fiberglass Batts + 1 ½ inch rigid XPS in south wall;  estimated R-11          original insulation in remaining walls

Infiltration		1724 cfm @ 50 pa	1015 cfm @ 50 pa							10.8 ACH @ 50 pa	6.9 ACH @ 50 pa

Windows 		Dual pane 		Dual Pane, Vinyl Framed Energy Star Windows 				Vinyl Framed 		Installed on south and east							.55 U-Factor		0.29 U-Factor								0.67 SHGC		0.21 SHGC

Space Heating		60% AFUE Gas		0.95 AFUE Sealed Combustion Gas Furnace

A/C	 		SEER 8, EER 6		SEER 16.5, EER 13

Ducts			Leaky R-4  		"Tight,” R-8 insulated tested to 5% leakage @ 25 Pa

BY SYSTEM		EXISTING		ENERGY EFFICIENT REMODEL

Thermostat	 	Non-programmable	Energy Star Programmable Thermostat

Spot Ventilation		None 			Energy Start Low Sone Fans with Timer Controls

Water Heating		.62 EF 50 gal. Gas 	62 EF	50  gal. Gas Water Heater

Lighting (units)		 Incandescent		100% hardwired Energy Star Compact Fluorescent

Ceiling Fans	 	Incandescent		Energy Star with pin-based Energy Star CFLs

Range Hood		Standard			Energy Star

Dishwasher	 	None			Energy Star EF = .63

Refrigerator		Standard			Energy Star

Solar PV 		None			1,673 watt AC system (estimated 2,460 kWh/yr)

HERS Rating		194			29

The BEopt analysis of the HfH home showed that the package of energy efficiency upgrades, including the PV system, is estimated to reduce the home’s annual electricity use by up to 93% , its annual natural gas consumption by up to 74% , and its average peak demand 80% compare to the estimated energy use .  The home was sold and occupied in July, 2011.

Homes by Town (HBT) DER

SMUD worked with Homes by Town (HBT) on a foreclosure under the City of Elk Grove’s VPP program. The home was originally built in 1989, has 3 bedrooms, 2.5 baths, and is approximately 1,500 square feet.  A list of efficiency measures incorporated into the project is found in Table 6 below.

Table 6.  Homes by Town Existing Vs. DER Specifications

BY SYSTEM		EXISTING 		ENERGY EFFICIENT REMODEL

Air Sealing		None			Air Sealed the attic

Attic 			R-30			R-38 in cathedral ceiling area & R-49 flat in ceiling area  						Radiant Barrier roof sheathing

Infiltration		Unknown		744 cfm @ 50 pa; 4.3 ACH @ 50 pa

Space Heating	 	0.78 AFUE Gas		0.95AFUE Sealed Gas Combustion Furnace

A/C	 		SEER 10, EER 8		SEER 15, EER 12.5

Ducts			R- 5 insulation		 R-8 insulated 								25% leakage @ 25 pa 	3.75% leakage @ 25 pa

Thermostat	 	Existing			Energy Star Programmable Thermostat

Lighting (units)		Incandescent		100% hardwired Energy Star (CFLs)

Ceiling Fans	 	Incandescent		Energy Star CFLs

Dishwasher	 	Existing			Tier 2 (EF = .69) Energy Star

HERSII Rating		174			107

The HBT BEopt simulation showed 33% annual energy savings, including an estimated 44% electric use savings and 18% natural gas use savings, and 49% reduction in average peak demand.  The HBT DER was sold and occupy in July, 2011.

RESULTS TO DATE

The DERs’ electric and natural gas usage have been monitored since occupancy.  Since all the DER projects were abandoned homes without utility bill data comparisons to pre-retrofit consumption could not be made. As expected, electricity and natural gas use varied greatly among the DER homeowners (see Table 7 below).

Table 7. DER Avg. Monthly Electricity and Natural Gas Use Compared to SMUD Average  Residential Electricity Use and PG&E Average Residential Natural Gas Use

|  | DER Avg. Monthly Electric Use (kWh) | % over/under SMUD Avg. Residential Customer Use (750 kWh) | DER Avg. Monthly Natural Gas Use | % over/under PG&E Avg. Monthly Residential Natural Gas Use (41 Therms) |
| --- | --- | --- | --- | --- |
| Greenbuilt | 550 | -27% | all electric home |  |
| Jean | 908 | 21% | all electric home |  |
| HfH* | 464 | -38% | 30 | -27% |
| 32nd Ave | 632 | -16% | unavailable |  |
| Mascot | 922 | 23% | 21.5 | -48% |
| HbT* | 721 | -4% | 51 | 24% |

*less than one year of data

Based on a bill analysis, it appears that a majority of the DERs’ electricity use is being driven by miscellaneous plug loads with non-peak month electricity use between 60 to 96% of  peak month electricity use. (see Table 8  below)

Table 8. DER Peak Monthly vs. Non-Peak Monthly Electivity Use

|  | Summer (May-Sept) Monthly kWh | Winter Monthly (Nov-March) Monthly kWh | Spring/Fall kWh | % Spring/Fall |
| --- | --- | --- | --- | --- |
| Greenbuilt |  | 704 | 422 | 60%** |
| Jean |  | 1116 | 698 | 63%** |
| HfH* | 557 | 417 |  | 78% |
| 32nd Ave | 767 |  | 526 | 69% |
| Mascot | 946 |  | 904 | 96% |
| HbT* | 537 | 614 |  | 78% |

*less than a year’s worth of data

** All electric homes’ Spring/Fall electric usage compared to highest use winter months

Although the summer of 2011 was unusually mild in Sacramento with only six days over 100° F and no days over 105° F,   monitored data collected during the summer’s only “heat storm, “  July 3-5, with an average high temperature of 102° F showed that the DERS’ average peak demand (4-7pm)  ranged from -1.2 kW to  3.87 kW .   Five of the six DERs showed significant average 4-7 peak demand savings when compared to monitored SMUD residential gas and electric heated single-family homes (see Table 9 below)

Table 9.  DER vs. SMUD Residential Electric & Gas Heated Single Family Home (SFH) Customers Average Peak Demand (kW) July 3-5, 2011 4-7 pm

|  | Avg. kW | Electric/Gas Heated SFH Customer Avg. kW | % Difference |
| --- | --- | --- | --- |
| Greenbuilt* | -1.2* | 3.39 | -135% |
| Mascot | 3.05 | 3.29 | -7% |
| Habitat* | 0.6* | 3.29 | -82% |
| 32nd Ave | 1.8 | 3.29 | -45% |
| HBT | 3.87 | 3.29 | 18% |

*  PV production contributed 1.43 Average kW to the Greenbuilt DER and 0.60 kW to the Habitat DER during the July 3-5, 2011 4-7 pm peak period.

DERs are not inexpensive propositions.  Costs for the six DERs ranged from a high of $42,000 to $25,000, not unexpected given the fact that DERs involved major work and equipment replacement.  As mentioned, all six of the SMUD DER projects involved abandoned, foreclosed homes that required major renovation to make them “market ready,” including major structural repair and re-design.  For example, all of the projects required extensive interior repairs; three of the projects required a new roof; and so on.  However, the cost of a DER’s efficiency upgrades only represents a portion of the cost of a major renovation of a home, especially when major repairs and equipment replacement is required.  The energy efficiency portion of the four DER projects was a fraction of the total cost of the project (see Table 10 below):

Table 10. Total DER Project Costs vs. Energy Efficiency Upgrade Costs

Total Project Cost		Energy Efficiency Upgrade	% of Total Cost

Greenbuilt	$141,000				$42,000				30%

Mascot		$ 86,050					$25,000				29%

Jean		$120,000				$40,800				34%

32nd Avenue	$ 77,000					$26,769				35%

Habitat		$184,386				$24,635				13%

HBT		$ 66,500					$16,957				25%

LESSONS LEARNED

DERs have the potential to dramatically reduce an existing home’s energy use and peak demand. Based on the experience of the SMUD DER projects, a standardized package of upgrades could result in up to 60% annual energy savings, especially for Sacramento area homes built before 1978 (homes built before the introduction of the California Title-24 Standards). Furthermore, the use of energy efficiency “packages,” could provide predictable energy savings in an easy to understand format for DER contractors to use and homeowners to understand. Such a DER package would include:

•	Air Sealing the home to a minimum 7.5 Air Changes per Hour (@ 50 pa of pressure

•	R-38 attic insulation

•	Energy Star Windows (.30 U-Factor and Solar Heat Gain Coefficient)

•	“Right sized” (ACCA Manual D) SEER 14 air conditioner, 0.95 AFUE furnace or 9.5 HSPF Heat Pump with tight (less than 6% leakage), with R-8 insulated

•	.65 EF Gas Storage Water heater or 2.0 COP Heat Pump Water Heater

•	Energy Star Hard Wired CFL Fixtures

Using a “package approach” for DERs also has important implications for utility program planning.  To date, utility whole home efficiency programs have emphasized or relied largely on energy simulation to determine incentive levels.  In fact, SMUD’s Home Performance Program was mandated to use Title-24 Time Dependent Valuation (TDV) by the California Energy Commission (CEC).  The shortcomings of energy simulation software are well known – it’s time consuming, expensive, does not accurately predict bill impacts and can be “gamed” – simulation results can be manipulated to show exaggerated savings results.   Furthermore, energy simulation should be completed by trained, experienced professionals.  Asking home improvement contractors to become experts in energy simulation and rely on simulation estimates is unrealistic and will lead to problems in the field and confuse home owners.  Relying on energy simulation estimates could also result in over inflated utility program energy savings results. Energy simulation should be used to develop DER packages for a variety of climate zones and building vintage types. These DER packages should then be tested in the field to verify energy savings and the DER packages modified, if necessary based on field experience. The Department of Energy has suggested such an approach with the publication of “Energy Savings Measure Packages: Existing Homes.”

DER packages should also be designed to reduce utility peak demand, meaning that the DER package results in the installation of “right-sized,” reduced tonnage air conditioning units.  Quite simply, reduced air conditioning tonnage results in lower peak demands and energy use and doesn’t require energy simulation to estimate savings.  Redding Electric Utility has pioneered such an approach with impressive results to date, averaging 2.5 kW savings per home in their home performance program.

Utility planners also need to account for the contribution made by PV systems, especially in reducing a home’s peak demand.  Although PV systems may displace kWh sales and revenues they provide critical peak power.  PV system peak contributions are typically unrecognized not only by utility resource planners but utility efficiency staff.  The results from the Greenbuilt and HfH DERs show how PV production can result in near or zero peak homes even in late afternoon situations.

The extensive work involved in DERs incurs high costs.  DER efficiency measure costs can be mitigated if included in major renovation or rehabilitation projects, such as turning abandoned, foreclosed properties into marketable properties.  Moreover, to work, DERs require low interest, long-term financing. With the demise of the PACE program there is only one low interest, long-term financing option available – the Energy Efficient Mortgage (EEM).  EEMs were created under the Carter Administration in 1978 but have languished due to indifference on the part of real estate industry and lack of promotion. Currently 30-year mortgages interest rates are at historically low levels (< 4%) and represent an unprecedented opportunity to finance DERs under the EEM.  An analysis of the six DER Demonstration projects shows that using the low interest loans available through an EEM provides positive returns on investment and positive cash flow for homeowners, especially when combined with generous utility home performance incentives (see Table 11 below).

Table 11. Cash Flow and Return on Investment (ROI) of DERS with 4.25% EEM

|  | GreenBuilt | Mascot | Jean | Habitat | 32nd Ave | HBT |
| --- | --- | --- | --- | --- | --- | --- |
| EE/PV Costs | $60,813 | $25,000 | $40,759 | $24,000 | $26,789 | $16,957 |
| Loan Amt (10% down) | $54,732 | $22,500 | $36,683 | $23,160 | $24,110 | $15,261 |
| Down Payment | -6,081 | -$2,500 | -4,076 | -$2,400 | -2,679 | -1,696 |
| Annual Mortgage Payment | -$3,231 | -$1,328 | -$2,166 | -$1,367 | -$1,423 | -$901 |
| First Year Utility Savings (2.5% Annual Inflation Rate) | $2,444 | $1,264 | $1,686 | $1,204 | $2,240 | $737 |
| Utility Incentives | $11,235 | $9,000 | $5,000 | $9,000 | $5,000 | $3,000 |
| Fed. Tax Credits | $5,173 | $500 | $500 | $0 | $500 | $500 |
| Mortgage Deduction (25% Federal Tax Rate) | $577 | $237 | $387 | $244 | $254 | $161 |
| First Year Net Cash Flow | $10,117 | $7,173 | $1,331 | $6,681 | $3,892 | $1,801 |
| 10-Yr Cumulative Cash Flow | $5,663 | $7,954 | $1,969 | $10,891 | $15,716 | $2,428 |
| First Year ROI | 18.48% | 31.88% | 5.63% | 28.85% | 16.14% | 11.80% |

Until recently not all the elements were in place to drive the EEM.  It is the opinion of this author that an indifferent, sometimes hostile real estate industry and a lack of certified home energy raters (HERS) and home performance contractors have made it difficult for homebuyers to take advantage of the EEM.  The nation-wide push for home performance created by the Obama Administration and State and utility home performance programs represents an unprecedented opportunity to realize the potential of the EEM.  To date, state and utility home performance programs have concentrated their efforts on existing homeowners, rather than the re-sale market.  ESource reports that there has only been one utility sponsored EEM program, PG&E’s Time of Sale Energy Renovation (TOSER) Program, which was offered by between 1999 and 2001.  During that period 4,804 EEMs were completed and total estimated energy savings were the following:

•	15.7 million kWh (15.7 GWh) per year;

•	1.84 million therms per year; and

•	Electricity demand savings totaling 3.73 average megawatts.

In addition to the high costs of DERS and indifferent real estate market, utility home performance programs will labor with low participation rates given current economic conditions that have large numbers of homeowners with negative equity.  It is unrealistic to expect large numbers of home owners to invest in their homes, especially for energy savings reasons, until the real estate market improves, an unlikely prospect in the near term. However, more than 4 million existing homes are sold annually.  Each sale represents a unique opportunity to improve the energy performance of the home. If state and utility home performance programs were expanded to include EEMs, not only would new home owners realize cost effective energy saving improvements to their new homes, but home performance contractors (and HERS raters) could see steady business.  The re-sale market represents a market that could provide contractors steady and predictable work with which to grow their businesses.  It could also lead to greater homeowner interest in energy performance and help transform the market.  Finally, the re-sale market is the only market that can produce the numbers needed to affect significant energy savings in a short period of time.

Another promising area for DERS would be major remodeling projects, such as additions, and kitchen and bathroom remodels. Major remodeling projects typically entail extensive structural modifications to the home and often require new equipment, and they are usually very costly.  A DER package of energy efficiency upgrades would represent a minor portion of the total remodel cost and potentially deliver significant energy and utility bill savings to the homeowner.  The homeowner would also gain the non-financial benefits associated with increasing a home’s performance, such as increased comfort and reduced maintenance costs.

Research was supported by the U.S. Department of Energy Building America Program.